Flood Clean Up Instructions

BEFORE DOING ANYTHING…the structure should be inspected to assure it is safe to enter.  Check for structural damage to see if it is safe to enter the building.  Watch for electrical shorts and live wires.  Electrical safety is most important in floods.  Make sure that electrical service is DISCONNECTED and CANNOT be turned on before entering any structure.  Turn off any outside gas lines at the tank or meter, and let the building air out for several minutes to remove gas fumes.

###### Clean Up

- See that everyone is out of danger of new flood crests, falling buildings, fire or other hazards.

- Contact your insurance agent immediately.  Give your name, address and a phone number where you can be reached.

- Take pictures of the damage before beginning clean up.

- Keep accurate records.  List all clean-up and repair bills, flood-related living expenses and actual losses, such as furniture, appliances, clothing, etc

- Adjuster will assess damage to house.  Owner should sign proof-of-loss statement.  Additional damages can be added when found.  If you have a question or problem with your insurance carrier, contact the Missouri Department of Insurance: 1-800-726-7390.

Electrical Systems

- Be sure utilities are disconnected before entering the building for the first time.

- Disconnect main switch and all circuits. If the main switch is located in the basement, be sure all flood water is pumped out BEFORE attempting any work on electrical systems.

- Remove electrical outlet covers and clean all outlets and fuse or multi-breaker boxes.

- Dry contacts and spray with cleaner/lubricant.

- Have an electrician check for ground faults and other unsafe conditions and equipment before reconnecting systems.  Equipment and wiring that appears to be safe soon after flooding may fail prematurely and cause a fire or shock hazard.  Replacement is often the best option.  Circuit breakers that have been submerged should be replaced.

Carpets and Rugs

- Carpets and rugs may be cleaned best by professionals.

- To clean them yourself, pull up water-logged carpets, rugs and pads and dry outside on a clean, flat surface, such as a concrete driveway.  If the rug is placed face down, stains will wick to the back instead of to the face yarns.

- Hose off and, if badly soiled, add detergent.  Work detergent into carpet with broom and rinse well. Remove as much water as possible quickly using steam, fans or water-extraction equipment.  Take care to avoid electrical shock.

- To discourage mildew and odors, rinse with a solution of two tablespoons of chlorine bleach per gallon of water.  If the carpet is wool, do NOT add bleach.

- Dry carpet and floor thoroughly before carpet is replaced.  If carpet is put down wet, it may mildew. Carpet and backing may shrink.

- Discard all padding.

Subfloors

Layers of submerged plywood subfloors may separate. Sections that separate must be replaced to keep floor covering from buckling. When floor coverings are removed, allow subflooring to dry thoroughly (it may take several months). Check for warping before installing new flooring.

Wood floors:

- Carefully remove a board every few feet to reduce buckling caused by swelling. Consult a carpenter about removal techniques for tongue-and-groove boards.

- Clean and dry floor thoroughly (may take several weeks or months) before replacing boards and attempting repairs.

Tile and sheet-vinyl floors:

- If submerged subfloor is wood, floor covering probably should be removed so subflooring can be replaced. If floor has not been soaked, loose tiles may be re-cemented after floor is thoroughly dry.

- If subflooring is concrete, removing floor covering will speed drying of slab. Removal may not be necessary if it would ruin an otherwise unharmed material.

- If water has seeped under loose sections of sheet flooring, remove entire sheet.

- Contact a reputable dealer to find out what solvent and technique will loosen the adhesive with the least damage to the floor. Ease of removal depends on the type of material and adhesive.

Information and Referrals

- Contact local, state and federal offices for help and answers to specific clean-up questions.

- Your University Outreach and Extension center can help with food and water safety, cleanup and restoration questions or referrals.

- ParentLink offers parents and others with resources to help children cope: 1-800-552-8522.

Furniture

Take furniture outdoors to clean. Hose or brush off mud. All parts (drawers, doors, etc.) should be removed. Remove or cut hole in back to push out stuck drawers and doors.

Dry slowly out of direct sunlight (hot sunlight will warp furniture).  It may take several weeks to fully dry.

### Cleaning and Disinfecting

Wash exposed skin parts (hands, feet, etc.) frequently in purified water. Wear rubber gloves for extra protection against contamination. As flood waters recede, use a disinfectant to clean walls and woodwork from top to bottom. A 3-gallon garden sprayer works well. One cup of household chlorine bleach per gallon of water can be used as a disinfectant. Scrub with a brush to help remove mud and silt. Rinse with clean water. Dry thoroughly. If utilities are on, use heater, fan or air conditioner to speed drying.

Household Appliances

Submerged appliances must be cleaned and dried before starting.

With electricity or fuel turned off, unplug and open as much as possible to rinse or wipe clean and let dry. Tilt to drain and aid quick drying. Three days to a week is necessary for drying. Appliance repair person should check before reconnecting. Most motorized appliances can be saved.

Flood-Damaged Walls

- Remove water from structure as rapidly as possible.

- Remove interior surface of insulated walls to point above water height.

- Remove and discard wet insulation.

- Treat interior wall studs and plates with disinfectant to prevent growth of decay-causing organisms.

- Provide ventilation by opening windows and doors and using fans.

- Leave walls open for up to four weeks or until they have thoroughly dried.

- Select replacement materials that will withstand future floods.

- Delay permanent repairs until buildings are thoroughly dry (may be several weeks).

- Control mildew in the weeks and months that follow flood.

Clothing and Linens

Even if your washing machine did not get wet, do not use it until you know that the water is safe enough to drink and that your sewer line works.  Before you wash clothes in the washing machine, run the machine through one full cycle.  Be sure to use hot water and a disinfectant or sanitizer.  Take clothes and linens outdoors and shake out dried mud or dirt before you wash them.  To prevent a drain clog, hose off muddy items to remove all dirt before you put them in the washer.  Check the labels on clothes and linens, and wash them in detergent and warm water if possible.  Adding chlorine bleach to the wash cycle will remove most mildew and will sanitize the clothing, but bleach fades some fabrics and damages other fabrics.  You can buy other sanitizers, such as pine oil cleaners, at the grocery store to sanitize fabrics that cannot be bleached.  If the label says “Dry Clean Only,” shake out loose dirt and take the item to a professional cleaner.  Furs and leather items are usually worth the cost of professional cleaning.  If you want to clean leather yourself, wash the mud off and dry the leather slowly away from heat or sunlight.

Cleaning Mold and Mildew

Mold, mildew and bacteria are common following floods and other water damage. If unchecked they can lead to sanitation and health problems.  The walls, floors, closets, shelves, contents-every flooded part of your house-should be thoroughly washed and disinfected.   In most cases, household cleaning products will do the job

if you use them correctly.  Check the label on the products to see how much to use.  Some products shouldn’t be used on certain materials; the label will tell you that.  Apply cleaner and give it time to work before you mop or sponge it up.  Follow directions and all safety precautions on the container.  After cleaning a room or item, go over it again with a disinfectant to kill the germs and smell left by the floodwaters.  You may also need to get rid of mildew, an unwelcome companion to moisture that shows as fuzzy splotches.

Cleaning tips

Tackle one room at a time. A two bucket approach is most efficient: use one bucket for rinse water and the other for the cleaner. Rinse out your sponge, mop, or cleaning cloth in the rinse bucket.  Wring it as dry as possible and keep it rolled up tight as you put it in the cleaner bucket.  Let it unroll to absorb the cleaner. Using two buckets keeps most of the dirty rinse water out of your cleaning solution.  Replace the rinse water frequently.

Walls

Start cleaning a wall at the bottom or where the worst damage was.  If you did not have to remove the wallboard or plaster, you may find it the wallboard or plaster won’t come clean and you will want to replace it rather than clean it.  If you have removed the wallboard or plaster, wash the studs and sills and disinfect them.

Furniture:

Solid wood furniture can usually be repaired and cleaned, but wood veneer often separates and warps.  Wood alcohol or turpentine applied with a cotton ball may remove white mildew spots on wood.  Cream wood restorers with lanolin will help restore good wooden furniture parts.  Upholstered furniture soaks up contaminants from floodwaters and should be cleaned only by a professional.  Unless the piece is an antique or especially valuable, upholstered furniture soaked by floodwaters should probably be thrown out.